Office use only:

Control Number: 29

Assigned Group:

Initial Screening :

Ballot:  Pass: ______/ Fail: _____

Effective for Race Year: 2018

2018 Rule Change Proposal

Author:  Dutch Squires

APBA #    1621

E-mail:    megabucks83@comcast.net

Telephone:   303 987 0968

Date:	1/10/18

Note: Proposals must be submitted to the Inboard Office by December 1, 2017 to be considered.

Save and E-mail completed form to: inboardracing@apba.org

US mail to   APBA Inboard Office    PO Box 71, Washington, MI   48094

Check all that apply:

General Safety Rule

General Racing Rule			x

Stock Class Technical Rule *		x

Modified Class Technical Rule *		x

Affected Class(es):

## Specific Rule Information:  [Note: All fields  must be completed for consideration.]

Author”s VERY BRIEF Summary of Proposed Action:  Simplify inspections a national events  Summer Nationals   Westerns  Easterns

Affected Rule:  42.3   43.5   43.7   45.1.27   45.2.27   54.3.14   54.4.14   54.4.15

Proposed rule: Add    rule  6.6.15.3

APBA Inboard National Event Inspection Protocol

At a National Event all classes shall be inspected under the Level 1 procedure listed below. However, 1 class that shall be drawn from a hat at the driver's meeting by the Referee will be inspected under the Level 2 procedure. This class shall be announced after it has finished its heats of competition and has been sealed. If a modified class is drawn, its rule set may allow for a Level 1 inspection to be determined by the Inspector.

Levels of Inspection

Level 1: Any measurements or procedures the inspector chooses without removing the head/heads. Any 2-stroke engine must have the head/heads removed for a physical measurement of displacement.

Level 2   Any measurements or procedures the inspector chooses with the head/heads removed, but short of removing the short block from the hull.

Level 3   A complete inspection that may include removing the short block from the hull.

This protocol does not preclude the referee or the inspector from the right to inspect any equipment, for any reason, at any time, at any level.  All levels of inspection allow the inspector discretion to choose the number of measurements or procedures he wishes to perform within the class rule set. In the case of a protest or a record being set a complete level 3 inspection is recommended.

Reason for change:  simplify inspections at national events

Note this rule would require some minor clean up of rules:

42.3 ( add recommended) Minimum inspection procedure for 1.5 Litre Stock Toyota.

43.5 (add recommended) 7 point Minimum Inspection Procedure for 2000cc Ford Pinto.

45.1.27 In the event that (Delete---  a national championship, a divisional championship, or) a  record is established, the engine must be dismantled to determine legality of the parts.

45.2.27 In the event that (Delete---- a National Championship, a Divisional Championship, or) a record is established, the engine must be dismantled to determine legality of the parts.

54.3.14 (add recommended)7 Point Minimum Inspection Procedure for 283 cu. in. engine

54.4.14(add recommended) 7 Point Minimum Inspection Procedure for 305 Cubic Inch Motor

54.4.15 (add recommended) 6 Point Minimum Inspection for Boat